E85 Z4M DME REMOVAL PROCEDURES

NOTE: We recommend that you disconnect your battery for this procedure.

At a minimum, open the hood, lock the car, and wait at least 15 minutes for the car to go to sleep.

- Find the DME box on the driver’s side forward of the firewall.

Remove the FOUR (4) T25 Torx screws and store them in a safe place.

- Pivot the cover up away from the engine and lift it to remove.

3. If you car has the black retainer plastic clip over the DME, carefully lift the tabs around the edge and remove it. Store it to replace later. There are two tabs holding the DME in the slot. Pull the DME up past these tabs to remove.

4. The wiring harness plugs are attached to the DME with slide locks on either end.

5. Slide the lock handles to the outsides and remove the harness. Your DME is ready to remove.

DO NOT try to start the car with the DME removed!

Please fill in the following information and include this page with your DME:

Name:

Order #				 (if you have it)

Address:

City:

State:

Zip:

Phone:

Product Requested:	N/A Software	S/C Software	Reflash

Other:

Headers installed? (  Yes  /  No  )

Fuel Octane Used:	91		93/94		Other:

Comments:

Shipping suggestions:

٠Carefully wrap and pack your DME before shipment. It’s case is very sturdy, but the plugs/pins can be damaged.

٠Use a shipping carrier who allows tracking.

٠If sending internationally, mark the package type as “Repair and Return” and with a value of $20.

ESS DME Shipping Addresses

Inside the United States:

ESS Performance Products USA

16845 N 29th Ave

Suite #1-303

Phoenix, AZ 85053

858-314-2954

Outside the United States:

ESS Performance Products A/S

Rive

1798 Aremark

Norway

+4741558555